## Slide 1
BICS 2304 | Computer Architecture & Assembly Language | Section 04
JUPITER
Wearable Heat Stroke &
Dehydration Prevention System
Adam Fawwaz Bin Sazalizam (2416969) Ahmad Fawwaz Bin Abdul Kadir (2418497) Wan Abdullah Mikhaiel Bin Wan Shamsuddin (2416229) Alfyan Shawn Bin Jasni Shirlin (2417841)
Lecturer: Yasir Mehmood

## Slide 2
System Overview
What is Jupiter?
A simulated wearable IoT device designed for outdoor workers and athletes in tropical climates like Malaysia.
The system continuously monitors physiological data and environmental conditions, triggering alerts before a heat stroke or dehydration event occurs.
Implementation
Simulated in MIPS Assembly Language using MARS IDE.
Sensor inputs entered via console each monitoring cycle.
Actuator responses printed as console output.
3+
Sensors monitored
per cycle
4
Actuator responses
simulated
4
Priority levels
in decision engine
5
Test cases
all passing

## Slide 3
Hardware Components
SENSORS
MAX30205
Body Temperature Sensor
0–50°C, ±0.1°C accuracy
MAX30102
Pulse Rate / Heart Rate
30–250 BPM, I2C interface
MPU6050
Accelerometer & Gyroscope
Fall detection via G-Force spike
Timer S4
Sustained Motion Timer
Tracks active minutes (software)
ACTUATORS
A1
Haptic Vibration Motor
Physical alert — brief pulse or continuous
A2
Hydration Reminder LED
Blinks when drink water trigger fires
A3
Cooling Vest Fan
Activates on heat stress condition
A4
GPS Broadcast (SIM800L)
SOS signal on fall/critical detection

## Slide 4
Priority Decision Logic
Conditions evaluated in order — highest priority first. First match wins.
P1 — Fall Detection
Condition: Accel > 100G AND Motion Timer = 0
Output: [Status: CRITICAL] → GPS SOS transmitted, program exits with code 10
P2 — Heat Stress Index
Condition: Heart Rate > 130 BPM AND Body Temp > 38°C
Output: [Status: Take a break] → Haptic motor continuous + Cooling fan active
P3 — Hydration Reminder
Condition: Motion Timer ≥ 15 minutes
Output: [Drink Water] → LED blinking + Haptic brief pulse + Timer reset to 0
P4 — Safe (default)
Condition: None of the above conditions are met
Output: [Status: Safe] → All actuators OFF

## Slide 5
System Flowchart

## Slide 6
Input Validation & Error Handling
How It Works
Only body temperature is validated (physiological bound).
Valid range: 0 to 50°C.
Any value outside this range triggers an error message and re-prompts the user.
The program loops internally until a valid value is entered — it never crashes or skips.
Console Output (TC-05)
[SENSOR S1] Enter Body Temperature (0-50 C): 120 [ERROR]: Out of human physiological bounds! Enter 0 to 50. [SENSOR S1] Enter Body Temperature (0-50 C): 37 [SENSOR S2] Enter Heart Rate (BPM): ...

## Slide 7
Test Case Results
Test Case
Inputs
Expected Output
✓
TC-01
Normal Safe
Temp=36, HR=80, Accel=15, Timer=2
[Status: Safe] — All actuators OFF
PASS
TC-02
Heat Stress
Temp=39, HR=140, Accel=10, Timer=4
[Status: Take a break] — Haptic + Fan active
PASS
TC-03
Hydration Alert
Temp=37, HR=85, Accel=12, Timer=15
[Drink Water] — LED blink + Haptic + Timer reset
PASS
TC-04
Fall / Critical
Temp=36, HR=75, Accel=110, Timer=0
[Status: CRITICAL] — GPS SOS + exit code 10
PASS
TC-05
Input Validation
Temp=120 (invalid) → retry with 37
[ERROR] message + re-prompt, then normal flow
PASS

## Slide 8
Work Distribution
Adam Fawwaz Bin Sazalizam
2416969 | Group Leader
Project coordination · Flowchart design · Body Temperature sensor module · Final integration
Ahmad Fawwaz Bin Abdul Kadir
2418497
Use case diagram · Pulse Rate sensor module · Heat Stress Index decision logic · Unit testing
Wan Abdullah Mikhaiel Bin Wan Shamsuddin
2416229
Hardware mapping table · Accelerometer sensor module · Fall detection logic · Decision & control testing
Alfyan Shawn Bin Jasni Shirlin
2417841
Display & status output module · Actuator subroutines (Haptic, LED, GPS) · Error handling · Code review

## Slide 9
Conclusion
✓
3 sensors + 4 actuators — all project requirements met
✓
Priority decision engine with 4 conditions — P1 (critical) through P4 (safe)
✓
Input validation with error handling and recovery loop
✓
Modular code — 9 procedures/subroutines with clear register convention
✓
All 5 test cases pass as documented in the test cases submission
Thank You